## Slide 1: Design and Modeling of Specialized Architectures
Yakun Sophia Shao
May 9th, 2016
Phd Dissertation Defense

## Slide 2: Moore’s Law

## Slide 3: CMOS Scaling is Slowing Down
http://www.anandtech.com/show/9447/intel-10nm-and-kaby-lake
180 nm
130 nm
90 nm
65 nm
45 nm
32 nm
22 nm
14 nm
10 nm

## Slide 4: CMOS Technology Scaling
Technological
Fallow Period

## Slide 5: Potential for Specialized Architectures
[Zhang and Brodersen]
16 | Encryption
17 | Hearing Aid
18 | FIR for disk read
19 | MPEG Encoder
20 | 802.11 Baseband

## Slide 6: Cores, GPUs, and Accelerators: Apple A8 SoC
Out-of-Core
Accelerators

## Slide 7: Cores, GPUs, and Accelerators: Apple A8 SoC
Out-of-Core
Accelerators

## Slide 8: Cores, GPUs, and Accelerators: Apple A8 SoC
Out-of-Core
Accelerators
Maltiel Consulting
estimates
Our estimates

## Slide 9: Challenges in Accelerators
Flexibility
  Fixed-function accelerators are only designed for the target applications.
Programmability
  Today’s accelerators are explicitly managed by programmers.

## Slide 10: Today’s SoC
OMAP 4 SoC

## Slide 11: Today’s SoC
OMAP 4 SoC
ARM Cores
GPU
DSP
DSP
System Bus
Secondary
Bus
Secondary
Bus
Tertiary
Bus
DMA
DMA
SD
USB
Audio
Video
Face
Imaging
USB

## Slide 12: Challenges in Accelerators
Flexibility
  Fixed-function accelerators are only designed for the target applications.
Programmability
  Today’s accelerators are explicitly managed by programmers.
Design Cost
  Accelerator (and RTL) implementation is inherently tedious and time-consuming.

## Slide 13: Today’s SoC
GPU/DSP
CPU
Buses
Mem
Inter-
face
Acc
CPU
Acc
Acc
Acc
Acc
Acc
Acc
Acc
Acc

## Slide 14: Future Accelerator-Centric Architectures
Flexibility
Design Cost
Programmability
How to decompose applications into accelerators?
How to rapidly design lots of accelerators?
How to design and manage the shared resources?
GPU/DSP
Big
Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores

## Slide 15: Contributions
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores
Accelerator-System
Co-Design
[Under Review]
Research Infrastructures for Hardware Accelerators [Synthesis Lecture’15]
Accelerator Design w/
High-Level Synthesis [ISLPED’13_1]
Aladdin: Accelerator Pre-RTL, Power-Performance Simulator
[ISCA’14, TopPicks’15]
MachSuite: Accelerator Benchmark Suite [IISWC’14]
WIICA: Accelerator Workload Characterization [ISPASS’13]
Instruction-Level Energy Model for Xeon Phi [ISLPED’13_2]

## Slide 16
Private L1/
Scratchpad
Aladdin
Accelerator
Specific
Datapath
Shared Memory/Interconnect
Models
Unmodified
C-Code
Accelerator Design
Parameters
(e.g., # FU, mem. BW)
Power/Area
Performance
“Accelerator Simulator”
Design Accelerator-Rich SoC
Fabrics and Memory Systems
Design Cost
Flexibility
Programmability
Aladdin: A pre-RTL, Power-Performance Accelerator Simulator
“Design Assistant”
Understand Algorithmic-HW
Design Space before RTL

## Slide 17: Future Accelerator-Centric Architecture
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores

## Slide 18: Future Accelerator-Centric Architecture
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores
Aladdin can rapidly evaluate large design space of accelerator-centric architectures.

## Slide 19: Aladdin Overview
C Code
Power/Area
Performance
Activity
Acc Design Parameters
Optimization Phase
Realization Phase
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Dynamic Data
Dependence Graph
(DDDG)

## Slide 20: Aladdin Overview
C Code
Optimistic
IR
Initial
DDDG
Idealistic
DDDG
Program
Constrained
DDDG
Resource
Constrained
DDDG
Power/Area
Models
Optimization Phase
Realization Phase
Power/Area
Performance
Activity
Acc Design Parameters

## Slide 21: From C to Design Space
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];

## Slide 22: From C to Design Space IR Dynamic Trace
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
0. r0=0 //i = 0
r4=load (r0 + r1) //load a[i]
r5=load (r0 + r2) //load b[i]
r6=r4 + r5
store(r0 + r3, r6) //store c[i]
r0=r0 + 1 //++i
r4=load(r0 + r1) //load a[i]
r5=load(r0 + r2) //load b[i]
r6=r4 + r5
store(r0 + r3, r6) //store c[i]
r0 = r0 + 1 //++i
…

## Slide 23: From C to Design Space Initial DDDG
0. i=0
1. ld a
2. ld b
3. +
4. st c
5. i++
6. ld a
7. ld b
8. +
9. st c
10. i++
11. ld a
12. ld b
13. +
14. st c
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
IR Trace:
0. r0=0 //i = 0
1. r4=load (r0 + r1) //load a[i]
2. r5=load (r0 + r2) //load b[i]
3. r6=r4 + r5
4. store(r0 + r3, r6) //store c[i]
5. r0=r0 + 1 //++i
6. r4=load(r0 + r1) //load a[i]
7. r5=load(r0 + r2) //load b[i]
8. r6=r4 + r5
9. store(r0 + r3, r6) //store c[i]
10.r0 = r0 + 1 //++i
…

## Slide 24: From C to Design Space Idealistic DDDG
0. i=0
5. i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
C Code:
for(i=0; i<N; ++i)
c[i] = a[i] + b[i];
IR Trace:
0. r0=0 //i = 0
1. r4=load (r0 + r1) //load a[i]
2. r5=load (r0 + r2) //load b[i]
3. r6=r4 + r5
4. store(r0 + r3, r6) //store c[i]
5. r0=r0 + 1 //++i
6. r4=load(r0 + r1) //load a[i]
7. r5=load(r0 + r2) //load b[i]
8. r6=r4 + r5
9. store(r0 + r3, r6) //store c[i]
10.r0 = r0 + 1 //++i
…
0. i=0
5. i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c

## Slide 25: From C to Design Space Optimization Phase: C->IR->DDDG
Include application-specific customization strategies.
Node-Level:
  Bit-width Analysis
  Strength Reduction
  Tree-height Reduction
Loop-Level:
  Remove dependences between loop index variables
Memory Optimization:
  Memory-to-Register Conversion
  Store-Load Forwarding
  Store Buffer

## Slide 26: From C to Design Space One Design
MEM
MEM
MEM
MEM
MEM
MEM
+
+
+
Resource Activity
Idealistic DDDG
Acc Design Parameters:
Memory BW <= 2
1 Adder
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c
Cycle
0. i=0
5.i++
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c

## Slide 27: From C to Design Space Another Design
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
MEM
+
+
+
+
+
+
+
Resource Activity
Cycle
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c
6. ld a
Acc Design Parameters:
Memory BW <= 4
2 Adders
Idealistic DDDG
0. i=0
5.i++
10. i++
11. ld a
12. ld b
13. +
14. st c
6. ld a
7. ld b
8. +
9. st c
1. ld a
2. ld b
3. +
4. st c
15. i++
16. ld a
17. ld b
18. +
19. st c

## Slide 28: From C to Design Space Realization Phase: DDDG->Estimates
Constrain the DDDG with program and user-defined resource constraints
Program Constraints
  Control Dependence
  Memory Ambiguation
Resource Constraints
  Loop-level Parallelism
  Loop Pipelining
  Memory Ports

## Slide 29: From C to Design Space Power-Performance per Design
Cycle
Power
Acc Design Parameters:
Memory BW <= 4
2 Adders
Acc Design Parameters:
Memory BW <= 2
1 Adder

## Slide 30: From C to Design Space Design Space of an Algorithm
Cycle
Power

## Slide 31: Aladdin Validation
C Code
Power/Area Performance
Aladdin
ModelSim
Design
Compiler
Verilog
Activity

## Slide 32: Aladdin Validation
C Code
Power/Area Performance
Aladdin
RTL Designer
HLS C Tuning
Vivado
HLS
ModelSim
Design
Compiler
Verilog
Activity

## Slide 33: Aladdin Validation

## Slide 34: Aladdin Validation

## Slide 35: Algorithm-to-Solution Time
 | Hand-Coded RTL | C-to-RTL
Programming Effort | High | Medium
RTL Generation | Designer Dependent | 37 mins
RTL Simulation | 5 mins | 
RTL Synthesis | 45 mins | 
Time to Solution per Design | 87 mins | 
Time to Solution (36 Designs) | 52 hours | 

## Slide 36: Algorithm-to-Solution Time
 | Hand-Coded RTL | C-to-RTL | Aladdin
Programming Effort | High | Medium | N/A
RTL Generation | Designer Dependent | 37 mins | 
RTL Simulation | 5 mins |  | 
RTL Synthesis | 45 mins |  | 
Time to Solution per Design | 87 mins |  | 1 min
Time to Solution (36 Designs) | 52 hours |  | 7 min

## Slide 37: Aladdin enables pre-RTL simulation of accelerators with the rest of the SoC.
GPU
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Big
Cores
Small Cores
GPGPU-Sim
gem5
...
gem5
…
Cacti/Orion2
DRAMSim2

## Slide 38: Accelerator Integration
ACC
MEM
Lane 0
Lane 1
Lane 2
Lane 3
ARR 0
ARR 1
BUF 0
BUF 1
Lane 4
SPAD Interface
CPU 0
CPU 1
L1 $
L1 $
L2 $
System Bus
MC
DRAM
SRC ADDR
DEST ADDR
LENGTH
Transfer Descriptors
CHAN 0
CHAN 3
Channel Selection
DMA

## Slide 39: Compute is only a part of the story

## Slide 40: Compute is only a part of the story
Accelerator-System Co-Design

## Slide 41: Accelerator Integration
ACC
MEM
Lane 0
Lane 1
Lane 2
Lane 3
ARR 0
ARR 1
BUF 0
BUF 1
Lane 4
SPAD Interface
CPU 0
CPU 1
L1 $
L1 $
L2 $
System Bus
MC
DRAM
SRC ADDR
DEST ADDR
LENGTH
Transfer Descriptors
CHAN 0
CHAN 3
Channel Selection
DMA
ACC
MEM
Lane 0
Lane 1
Lane 2
Lane 3
TLB
Cache
Cache Interface

## Slide 42: gem5-Aladdin: An SoC Simulator
ACC
MEM
Lane 0
Lane 1
Lane 2
Lane 3
ARR 0
ARR 1
BUF 0
BUF 1
Lane 4
SPAD Interface
CPU 0
CPU 1
L1 $
L1 $
L2 $
System Bus
MC
DRAM
SRC ADDR
DEST ADDR
LENGTH
Transfer Descriptors
CHAN 0
CHAN 3
Channel Selection
DMA
ACC
MEM
Lane 0
Lane 1
Lane 2
Lane 3
TLB
Cache
Cache Interface

## Slide 43: gem5-Aladdin Validation
Application
gem5-Aladdin
Vivado
HLS
Verilog
Flush
Latency
DMA
Latency
Acc Exe Latency
DMA
IP Block
FPGA
ARM
Core
Xilinx Zynq SoC
Kernel

## Slide 44: gem5-Aladdin Validation

## Slide 45: To DMA or To Cache?
Accelerator local memory

## Slide 46: DMA or Cache

## Slide 47: DMA or Cache

## Slide 48: DMA or Cache

## Slide 49: Conclusions
Architectures with 1000s of accelerators will be radically different; New design tools are needed.
We built Aladdin, an architectural level power, performance, and area simulator for accelerators.
We integrated Aladdin with gem5 to model the interactions between accelerators and the rest of the SoC.
These accelerator infrastructures open up opportunities for innovation on heterogeneous architecture designs.
Harvard University

## Slide 50: Contributions
GPU/DSP
Big Cores
Shared Resources
Memory
Interface
Sea of Fine-Grained
Accelerators
Small Cores
Accelerator-System
Co-Design
[Under Review]
Research Infrastructures for Hardware Accelerators [Synthesis Lecture’15]
Accelerator Design w/
High-Level Synthesis [ISLPED’13_1]
Aladdin: Accelerator Pre-RTL, Power-Performance Simulator
[ISCA’14, TopPicks’15]
MachSuite: Accelerator Benchmark Suite [IISWC’14]
WIICA: Accelerator Workload Characterization [ISPASS’13]
Instruction-Level Energy Model for Xeon Phi [ISLPED’13_2]

## Slide 51: Publications
Y.S. Shao, S. Xi, V. Srinivasan, G.-Y. Wei, D. Brooks, “An Holistic Approach to Accelerator-System Co-Design,” Under Review.
Y.S Shao and D. Brooks, “Research Infrastructures for Hardware Accelerators,” Synthesis Lectures on Computer Architecture, Nov 2015.
Y.S. Shao, B. Reagen, G.-Y. Wei, D. Brooks, “The Aladdin Approach to Accelerator Design and Modeling,” IEEE Micro TopPicks, May-June 2015.
Y.S. Shao, S. Xi, V. Srinivasan, G.-Y. Wei, D. Brooks, “Toward Cache-Friendly Hardware Accelerators,” SCAW’15.
B. Reagen, B. Adolf, Y.S. Shao, G.-Y. Wei, D. Brooks, “MachSuite: Benchmarks for Accelerator Design and Customized Architectures,” IISWC’14.
Y.S. Shao, B. Reagen, G.-Y. Wei, D. Brooks, “Aladdin: A Pre-RTL, Power-Performance Accelerator Simulator Enabling Large Design Space Exploration of Customized Architectures,” ISCA’14.
B. Reagen, Y.S. Shao, G.-Y. Wei, D. Brooks, “Quantifying Acceleration: Power/Performance Trade-Offs of Application Kernels in Hardware,” ISLPED’13.
Y.S. Shao and D. Brooks, “Energy Characterization and Instruction-Level Energy Model of Intel’s Xeon Phi Processor,” ISLPED’13.
Y.S. Shao and D. Brooks, “ISA-Independent Workload Characterization and its Implications for Specialized Architectures,” ISPASS’13.

## Slide 52: Acknowledgement

## Slide 53: Thanks!